- NFS client module + NFS server module

- Client and server module communicate using remote procedure call

- Virtual file system module provides the access transparency (How?)

- File identifiers in NFS are called file handles: File system identifier, i-node number, i-node generation number (to compensate for reusable i-node numbers)

- A client obtains the file handle when it requests: lookup, mkdir or create operation that results in mount

- VFS layer has one VFS structure for each mounted file system and one vnode per open file.

- vnode identifies inode (for unix system) for local file or file handle for remote file

- path name translation; caching is used to improve performance

- access is in blocks; prefetch to improve performance

- caching in both the client and server to achieve adequate performance; Server:

  - read buffer: if process sends a request to a page already in buffer, no need to access disk

  - read ahead in anticipation of access

  - delayed write : to guard against data loss unix synch operation is used to flush the altered pages every 30 seconds

  - Write thru or commit protocol is sued while write request comes in.

- Client caching:

  - Client uses caching for data it needs

  - Maintaining consistency with server becomes an issue

  - Timestamp method is used to validate the data before it Is used:

Tc is time when cache entry was validated; Tm is when block was last modified at the server; current time T – Tc < t, freshness interval then the it Is okay to use data; or Tm = Tc it is okay to use data.

Issue: What is optimal value of t? (predefined)

How to get Tm? (getattr)

12. Biodaemon: processes at client to perform read-ahead and delayed write.