## Slide 1: Arduino and Automotive Embedded Systems
B.Ramamurthy

## Slide 2: References
http://www.arduino.cc/
M. McRoberts. Beginning Arduino. Apress, 2010.
http://duino4projects.com/projects/car-projects/
http://www.practicalarduino.com/projects/vehicle-telemetry-platform
Many www.youtube.com Arduino tutorial videos
http://en.wikipedia.org/wiki/Atmel_AVR
https://code.google.com/p/opengauge/wiki/OBDuino
http://ecomodder.com/forum/showthread.php/obduino-mega-10300.html
http://playground.arduino.cc/Interfacing/Processing
http://arduino.cc/en/Tutorial/HomePage

## Slide 3: What is an Ardunio?
“A single-board microcontroller and a software suite for programming it.”
Arduino Uno:
  The hardware consists of a simple, open design for the controller with an Atmel AVR processor and on-board I/O support.
  The software consists of a standard programming language and the boot loader that runs on the board.
Arduino is a tiny embedded system that you can program to process between the device and the external components you connect to it.
Example1: connect a led to the output, switch to input, when a switch is pressed, the light is turned on, processor counts and turns it off after 30 seconds
Example2: Replace the switch with PIR (Passive InfraRed ) sensor that will trigger the light. .. A car dome light? An intruder alarm?
Simply put: An Arduino can be connected to LEDs, dot matrix displays, buttons, switches, motors, temperature sensors, distance sensors, GPS receivers, Ethernet modules, or just about any device…

## Slide 4: Why Arduino?
Is a convenient-sized unit for prototyping embedded system applications
Ardunio’s processor chip Atmel, Atmega are commonly used in automotive applications
Arduino+ Android + CAN (Controller Area Network) constitute the OpenXC platform promoted by Ford and other automotive companies
Multi-national involvement in chip design and manufacturing and in board design (Sweden: Chip, Italy: Board, USA: IDE, use: all over, across application domains)
Completely open source: both hardware and software (you can build your own Arduino board but cannot call it Arduino, that’s all)

## Slide 5: Arduino Board
Arduino board has an Atmel AVR(Alf Vegard RISC) processor
In the latest Arduino Uno version has Atmega8U2 a serial-usb converter, so can connect to game controller or a mouse too.
What else?
Arduino UNO R3 board, Original Manufacturer in Italy, ATmega328P Includes new pin configuration (SCL, SDA, IOREF)
Lets look at the board and understand its processor and IO capabilities.

## Slide 6: Memory
There are three pools of memory in the microcontroller used on avr-based Arduino boards :
  Flash memory (program space), is where the Arduino sketch is stored.
  SRAM (static random access memory) is where the sketch creates and manipulates variables when it runs.
  EEPROM is memory space that programmers can use to store long-term information.
The ATmega328 chip found on the Uno has the following amounts of memory:
  Flash 32k bytes (of which .5k is used for the bootloader)
  SRAM 2k bytes
  EEPROM 1k byte

## Slide 7: Programming Arduino
You will a Arduino IDE
You will write code in C
The step by step program can be developed in the IDE and downloaded the board through serial connector
Arduino IDE is a “Processing” application (We will discuss the Processing Java library tomorrow)
The programs are called sketches
There are so many ways you can program an Arduino: from Processing-based IDE on your computer, burn it into it, transfer from another Arduino…

## Slide 8: Shields
The Arduino can also be extended with the use of “shields”
Shields are circuit boards containing other devices (e.g. GPS receivers, LCD displays, Ethernet modules etc.)
These can simply plugged onto the top of the Arduino basic boards
Shields can plug-in on top of each other (connecting the I/O pins) thus providing extended functionality.
(You don’t have to use the shields, you can make you own external circuitry on a breadboard or PCB.)

## Slide 9: Types of Arduino
There are many types of Arduino: Uno , Due, Mini, Nano, Mega, etc.
There are many third party Arduino-compatible boards with different names:
OBduino (on-board diagnostics), Roboduino etc.
Most popular and versatile is Uno ( we have also used Due, for better timing response)
You prototype on the Uno, when you are satisfied with the application operation, just pop the 28-pin processor into an automobile host board or other hosts like Robots etc.

## Slide 10: Getting Started with Arduino
Download the latest IDE, unzip and double click on the unzipped folder to open it
You will see Arduino files and folders inside
Next plug-in your Arduino using the USB cable and ensure that the green power LED (PWR) turns on.
Windows will try to install the drivers for Arduino Uno and fail, don’t get upset..
Click on the Windows start button control panelSystem Device manager Arduino will appear with yellow exclamation mark right click and update software

## Slide 11: Updating the drivers (contd. From last slide)
Choose “Browse my computer for driver software”
Click Browse button
Navigate to the Arduino folder, Drivers folder and click OK
Windows will start installing the driver… when the security pops up a security message, click “Install this driver software anyway”
You should now see a message for successful installation.. Click Close
Now to open the IDE double click the Arduino icon.
We are all set to get started programming the device.
Lets write some simple programs and make sure our Arduino works.
Also look at http://arduino.cc/en/tutorial/foundations, you will need the understanding of these concepts for your project.
In general spend some time understanding the various aspects of the Arduino… read every document.

## Slide 12: Lets understand Arduino
http://arduino.cc
The tabs to look at are: Products, Learning, Reference, Blogs
You can submit your original projects for the world to see/use.