Project #1 – Booting Up Embedded XINU Operating System

CSE321: Embedded and Realtime Operating Systems                                                         Fall 2007

## 1. Objectives and overview of the project:

## Prepare a simple hardware system and embed in it a minimal operating system. The minimal operating system will be enhanced in the subsequent projects by other features. We will use WRT54GL the wireless router from Linksys [1] and Embedded XINU operating system [2] for this purpose. Students will

## (i) study the architecture of WRT54GL wireless router,

## (ii) modify the WRT54GL hardware to upload embedded XINU operating systems, and

(iii) test the embedded operating system using simple C programs.

## 2. Project Environment:

2.1 Operating system XINU: XINU ("Xinu Is Not Unix") is a small, academic operating system developed at Purdue University by Dr. Douglas E. Comer in the early 1980s for the LSI-11 platform; it has now been ported to a variety of platforms. Embedded XINU is an update of this project which attempts to modernize the code base (to ANSI-compliant C) and port the system to a modern architecture (specifically the MIPS architecture).

2.2 Hardware WRT54GL:  We will use wireless router WRT54GL as a host for embedded the software we will develop for enhancing the features of an embedded operating system. WRT54GL has a very interesting history the details of which can be found at [3]. The WRT54G is notable for being the first consumer-level network device that had its firmware source code released to satisfy the obligations of the GNU GPL. This allows programmers to modify the firmware to change or add functionality to the device. WRT54GL features a Broadcom MIPS processor  BCM5352 (200-250Mhz), a four port switch, 802.11b and 802.11g wireless LAN support, a Web interface for configuration of the router, 16Mbytes of RAM and 4Mbytes of flash memory. Any modification to the router function itself has to be done by updating the firmware on the flash memory. However we will use the RAM to load the embedded XINU.

2.3 Test Environment: The lab environment will be supported by other hardware and software components to provide cross-compiling and networking support. In order to compile Embedded MIPS kernels on a workstation that is not itself a MIPS processor, it is necessary to build and install an appropriate cross compiler. Any time you modify the embedded XINU, the recompiled software will have to be reloaded. A simple network configuration allocating IP address to the host with the cross-compiler, the wireless router that will host the embedded XINU and a common router that forms the network are shown in Figure 1.

Figure 1: Network to enable uploading Embedded XINU into WRT54GL (by D. You)

The Common Firmware Environment (CFE) [4] is the firmware developed by Broadcom for the BCM947xx SoC platform (among others). It is the first code that runs when the router boots and performs functions:

- Initializes the system

- Sets up a basic environment in which code can run

- Optionally provides a command line interface non-standard usage

- Loads and executes a kernel image

So, in normal operation, a user will not see CFE working at all; it will load the LinkSys kernel and send it on its merry way without hesitation. For us, however, CFE is crucial, because it provides us with the ability to load an image over the network using TFTP [5].

3. What to do?

  - Prepare Hardware

- Study the various components of the environment discussed above.

- Modify the Linksys WRt54GL hardware as follows: Obtain the parts as given in the list. Parts list:

| Quantity | Part Name | Details | Part / Model Number |
| --- | --- | --- | --- |
| 1 | LinkSys WRT54GL Router | 802.11b/g wireless broadband router | Linksys WRT54GL |
| 1 | Ribbon cable | 28 AWG, 10 conductor, 25' | Jameco 643508CM |
| 1 | IDC socket connector | 0.1”, 10 conductor | Jameco 32491CM |
| 1 | IDC shrouded header | 0.1”, 10 conductor | Jameco 67811CM |
| 1 | RS232 Transmitter/Receiver | IC 2DVR/2RCVR RS232 5V 20-DIP | DigiKey MAX233CPP-ND |
| 1 | DB9 Female | 22AWG,SOLDER CUP | Jameco 15771CM |
| 1 | DB9 Male | 22AWG,SOLDER CUP | Jameco 15747CM |

- Open the router.

- Attach the serial header.

- Wire serial header to MAX233A RS232 receiver/transmitter.

- Wire the DB9 connectors to MAX233A.

Make sure you solder the socket before mounting the chip itself.

  - Prepare software

  - Download and cross-compile the embedded XINU code.

  - Download TFTP for loading compiled XINU into the router via CFE.

  - Study the XINU code in the subdirectories.

  - Connect the serial port UART0 to the host (laptop/computer) with embedded XINU code and load it.

  - Configure the serial communication software.

  - Power-up the router.

  - Access the CFE and upload the embedded XINU.

3.3 Test the setup

Build and deploy XINU and examine the commands available. Write a simple test program “Hello World” and test the setup.

# Text boxes

IP: 192.168.0.101

IP: 192.168.0.130

Serial Communication

Network connection