## Slide 1: Clock-driven Static scheduling

## Slide 2: Basic concepts (1)
A periodic task is denoted by {tai, ei ,pi, Di} where the attributes are arrival time, execution time, period and relative deadline for task i
For example {0, 5, 12, 7} means
Arrival time
Execution time
deadline
period
Next arrival time
How will the timing diagram be for {1, 5, 12, 7} and for {0, 5,12, 12}? Discuss.

## Slide 3: N-periodic tasks
n periodic tasks with {tai, ei ,pi, Di} with i = 1..n need to be scheduled.
Since the four parameters known ahead the scheduling is static and a cyclic executive can be designed to schedule (& execute) the tasks so that they meet their respective deadlines.
Utilization Ui = ∑ (ei/pi)
Improve utilization by “slack stealing” to schedule a aperiodic task from the queue of aperiodic tasks.

## Slide 4: Rules for designing cyclic schedule
0. if Utilization >1, the tasks cannot be scheduled in the same processor.
If U is okay,
Hyperperiod H is lcm (pi) + these constraints
Frame f ≥ max(ei)
Frame f should evenly divide H.
There should be at least 1 frame between release time of a task and its deadline:
2f – gcd(pi,f) ≤ Di
Very often Di and Pi are same for periodic task. For simplicity in discussion we will assume this default setting.

## Slide 5: Example
ti | ri | ei | pi | Di
t1 | 0 | 1 | 4 | 4
t2 | 0 | 1.8 | 5 | 5
t3 | 0 | 1.0 | 20 | 20
t4 | 0 | 2.0 | 20 | 20
Given the task set above design the cyclic executive schedule
or clock driven static schedule.

## Slide 6: Cyclic Executive Design
Hyper-period is integer multiple of lcm(pi)= lcm (4,5,20,20) = 20
Frame is max of ei’s: max{1,1.8,2,2} = 2
f value of 2 evenly divides hyper-period value of 20
2f – gcd(pi,f) ≤ Di (satisfied as shown below)
  2X2 – gcd(4,2) = 4-2 <= 4
  2X 2 – gcd(5,2) = 4-1 <= 5
  2X2 – gcd(20,4) = 4-4 <= 20
  2X2 – gcd(20,4) = 4-4 <= 20
Design f = 2, hyperperiod = 20

## Slide 7
t1 | t3 | t2 | t2 | t1 |  | t4 | t4 | t2 | t2 | t1 |  | t2 | t2 | t1 |  | t2 | t2 | t1 | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
t1,t2,t3,t4
frame
Hyper-period
t1
t2
t1
t2
t1
t2
t1
t1,t2,t3,t4
repeats
Burn or base or aperiodic tasks
can use this slot

## Slide 8: Static Schedule
{
{ t1(1); t3(1)}
{t2(1.8}}
{t1(1); burn(1)}
{t4(2)}
{t2(2)}
{t1(1); burn(1)}
{t2(2)}
{t1(1);burn(1)}
{t2(2)}
{t1(1);burn(1)}
}
A cyclic executive of 10 frames with 2 slots each

## Slide 9
t1 | t3 | t2 | t2 | t1 |  | t2 | t2 | t1 |  | t2 | t2 | t1 |  | t4 | t4 | t2 | t2 | t1 | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
t1,t2,t3,t4
frame
Hyper-period
t1
t2
t1
t2
t1
t2
t1
t1,t2,t3,t4
repeats
Burn or base or aperiodic tasks
can use this slot
An alternate and better schedule.

## Slide 10: Summary
We studied formal design of a cyclic executive.
The algorithm discussed is proven method to generate a cyclic executive for a set of period tasks defining a RTOS.
Reference: Clock-driven scheduling
http://csperkins.org/teaching/rtes/lecture04.pdf