## Slide 1: Introduction to Hardware
B.Ramamurthy
bina@buffalo.edu
University at Buffalo

## Slide 2: Topics
One more example for state diagram design
Design alternatives
Block diagram of general purpose computer vs. embedded system
How is different for embedded systems?

## Slide 3: Design methods: Finite state machines
Finite state automaton (FSA), finite state machine (FSM) or state transition diagram (STD) is a formal method used in the specification and design of wide range of embedded and realtime systems.
The system in this case would be represented by a finite number of states.
Lets design the avionics for a drone aircraft.

## Slide 4: Drone aircraft avionics (simplified)
TAK
LAN
NAA
NAE
NAV
else
MA
else
TD
else
LO
else
EE
ED
MC
MA: Mission Assigned
TD: Target Detected
LO: Locked On
EE: enemy Evaded
ED: Enemy Destroyed
MC: Mission Complete
TAK: Take off
NAV: Navigate
NAE: Navigate & Evade
NAA: Navigate & Attack
LAN: Land

## Slide 5: Finite State Machine (FSM)
M = five tuple  { S, i, T, Σ, δ }
S = set of states
i = initial state
T = terminal state (s)
Σ = events that bring about transitions
δ = transitions
Lets do this exercise for the avionics for fighter aircraft

## Slide 6: State Transition table
 | MA | LO | TD | MC | EE | ED
TAK | NAV |  |  |  |  | 
NAV |  |  | NAE | LAN |  | 
NAE |  | NAA |  |  |  | 
NAA |  |  |  |  | NAE | NAV
LAN |  |  |  |  |  | 

## Slide 7: Design Choices/alternatives
Use the table to code a function with case statement
Or write a table-driven code
Which is better and why?
We will revisit this later…

## Slide 8: General Purpose Computer System
CPU - Central processing unit
ALU - Arithmetic and logic unit
ROM - Read only memory
RAM - Random access memory
Internal
Memory
Input
Output
CPU
Control
ALU
External
Memory

## Slide 9: Bus Architecture (in general purpose systems)
CPU
BUS
Memory
Parallel IO
controller
Serial IO
controller
Interrupt controller
DMA
controller
Why is this important? What is its relevance to embedded system?

## Slide 10: Embedded System
CPU
Control
ALU
Internal memory
Ports
This unit on a single chip is called a microcontroller

## Slide 11: On to Project 1
Project 1
C foundations: next class