## Slide 1: Implementation of Cyclic Executive
B. Ramamurthy

## Slide 2: Cyclic Executive Design 1 (pages 81-87)
Base tasks, clock tasks, interrupt tasks
  Base: no strict requirements, background activity
  Clock: periodic with fixed runtime
  Interrupt: event-driven preemption, rapid response but little processing
Design the slots
Table-driven cyclic executive

## Slide 3: Cyclic executive
Each task implemented as a function
All tasks see global data and share them
Cyclic executive for three priority level
The execution sequence of tasks within a cyclic executive will NOT vary in any unpredictable manner (such as in a regular fully featured Operating Systems)
Clock tasks, clock sched, base tasks, base sched, interrupt tasks
Each clock slot executes, clock tasks, at the end a burn task that is usually the base task
Study the figures in pages 83-86 of your text

## Slide 4: RT Cyclic Executive Program
Lets examine the code:
Identify the tasks
Identify the cyclic schedule specified in the form of a table
Observe how the functions are specified as table entry
Understand the scheduler is built-in
Learn how the function in the table are dispatched

## Slide 5: Task Specification to Cyclic Executive
Transform into hyperperiod, frame, slots
Design the cyclic executive
Then cyclic executive can be implemented by a table-driven
Or function-driven (simply a series of function calls).
We will look at a table-driven implementation.

## Slide 6: Implementation of a cyclic executive
#include <stdio.h>
#include <ctype.h>
#include <unistd.h>
#include <sys/times.h>
#define SLOTX 4
#define CYCLEX 5
#define SLOT_T 5000
int tps,cycle=0,slot=0;
clock_t now, then;
struct tms n;
void one() {
printf("Task 1 running\n");
sleep(1);
}
void two() {
printf("Task 2 running\n");
sleep(1); }

## Slide 7: Implementation (contd.)
void three() {
printf("Task 3 running\n");
sleep(1);
}
void four() {
printf("Task 4 running\n");
sleep(1);
}
void five() {
printf("Task 5 running\n");
sleep(1);
}

## Slide 8: Implementation (contd.)
void burn() {
clock_t bstart = times(&n);
while ((( now = times(&n)) - then) < SLOT_T * tps / 1000) { }
printf (" brn time = %2.2dms\n\n", (times(&n)-bstart)*1000/tps);
then = now;
cycle = CYCLEX;
}

## Slide 9: Implementation (contd.)
void (*ttable[SLOTX][CYCLEX])() = {
{one, two, burn, burn, burn},
{one, three, four, burn, burn},
{one, two, burn, burn, burn},
{one, five, four, burn, burn}};
main() {
tps = sysconf(_SC_CLK_TCK);
printf("clock ticks/sec = %d\n\n", tps);
then = times(&n);
while (1) {
for (slot=0; slot <SLOTX; slot++)
for (cycle=0; cycle<CYCLEX; cycle++)
(*ttable[slot][cycle])();
}}

## Slide 10: Summary
The cyclic executive discussed the scheduler is built-in. You can also use clock ticks RTC etc to schedule the tasks
In order use the cyclic executive discussed here in other applications simply change table configuration, and rewrite the dummy functions we used.