## Slide 1: CSE 486/586 Distributed Systems Failure Detectors
Steve Ko
Computer Sciences and Engineering
University at Buffalo

## Slide 2: Recap
Best Practices

## Slide 3: Today’s Question
How do we handle failures?
  Cannot answer this fully (yet!)
You’ll learn new terminologies, definitions, etc.
Let’s start with some new definitions.
One of the fundamental challenges in distributed systems
  Failure
  Ordering (with concurrency)
  Etc…

## Slide 4: Two Different System Models
Synchronous Distributed System
  Each message is received within bounded time
  Each step in a process takes lb < time < ub
  (Each local clock’s drift has a known bound)
  Examples: Multiprocessor systems
Asynchronous Distributed System
  No bounds on message transmission delays
  No bounds on process execution
  (The drift of a clock is arbitrary)
  Examples: Internet, wireless networks, datacenters, most real systems
These are used to reason about how protocols would behave, e.g., in formal proofs.

## Slide 5: Failure Model
What is a failure?
We’ll consider: process omission failure
  A process disappears.
  Permanently: crash-stop (fail-stop) – a process halts and does not execute any further operations
  Temporarily: crash-recovery – a process halts, but then recovers (reboots) after a while
We will focus on crash-stop failures
  Meaning, we assume there’s no other failure (e.g., network error). More failure types at the end of this lecture.
  They are easy to detect in synchronous systems
  Not so easy in asynchronous systems

## Slide 6: Why, What, and How
Why design a failure detector?
  First step to failure handling
What do we want from a failure detector?
  No miss (completeness)
  No mistake (accuracy)
How do we design one?

## Slide 7: What is a Failure Detector?
pi
pj

## Slide 8: What is a Failure Detector?
pi
pj
Crash-stop failure
(pj is a failed process)

## Slide 9: What is a Failure Detector?
pi
needs to know about pj’s failure
(pi is a non-faulty process
or alive process)
Crash-stop failure
(pj is a failed process)
pj
There are two styles of failure detectors

## Slide 10: I. Ping-Ack Protocol
pi queries pj once every T time units
If pj does not respond within another T time units of being sent the ping, pi detects/declares pj as failed
pi
pj
pj replies
ping
ack
If pj fails, then within T time units, pi will send
it a ping message. pi will time out within
another T time units.
Worst case Detection time = 2T
The waiting time ‘T’ can be parameterized.

## Slide 11: II. Heartbeating Protocol
pi
pj
pj maintains a sequence number
pj sends pi a heartbeat with incremented seq. number after every T time units
If pi has not received a new heartbeat for the past, say 3T time units, since it received the last heartbeat, then pi detects pj as failed
heartbeat
If T ≫ round trip time of messages, then worst case detection time ~ 3T (why?)
The ‘3’ can be changed to any positive number since it is a parameter

## Slide 12: In a Synchronous System
The Ping-Ack and Heartbeat failure detectors are always correct. For example (there could be other ways),
  Ping-Ack: set waiting time ‘T’ to be > round-trip time upper bound
  Heartbeat: set waiting time ‘3*T’ to be > round-trip time upper bound
The following property is guaranteed:
  If a process pj fails, then pi will detect its failure as long as pi itself is alive
  Its next ack/heartbeat will not be received (within the timeout), and thus pi will detect pj as having failed

## Slide 13: Failure Detector Properties
What do you mean a failure detector is “correct”?
Completeness = every process failure is eventually detected (no misses)
Accuracy = every detected failure corresponds to a crashed process (no mistakes)
Completeness and Accuracy
  Can both be guaranteed 100% in a synchronous distributed system (with reliable message delivery in bounded time)
  Can never be guaranteed simultaneously in an asynchronous distributed system
  Why?

## Slide 14: Completeness and Accuracy in Asynchronous Systems
Impossible because of arbitrary message delays
  If a heartbeat/ack is dropped (or several are dropped) from pj, then pj will be mistakenly detected as failed => inaccurate detection
  How large would the T waiting period in ping-ack or 3*T waiting period in heartbeating, need to be to obtain 100% accuracy?
  In asynchronous systems, delays on a network link are impossible to distinguish from a faulty process
Heartbeating – satisfies completeness but not accuracy (why?)
Ping-Ack – satisfies completeness but not accuracy (why?)
Point: You can’t design a perfect failure detector!
  You need to think about what metrics are important.

## Slide 15: Completeness or Accuracy? (in Asynchronous System)
Most failure detector implementations are willing to tolerate some inaccuracy, but require 100% completeness.
Plenty of distributed apps designed assuming 100% completeness, e.g., p2p systems
  “Err on the side of caution”.
  Processes not “stuck” waiting for other processes
But it’s ok to mistakenly detect once in a while since – (the victim process need only rejoin as a new process-—more later)
Both Hearbeating and Ping-Ack provide
  Probabilistic accuracy (for a process detected as failed, with some probability close to 1.0 (but not equal), it is true that it has actually crashed).

## Slide 16: Failure Detection in a Distributed System
That was for one process pj being detected and one process pi detecting failures
Let’s extend it to an entire distributed system
Difference from original failure detection is
  We want failure detection of not merely one process (pj), but all processes in system

## Slide 17: CSE 486/586 Administrivia
Will start grading PA1 soon.
PA2A due in roughly two weeks (Fri, 2/21)
Please use Piazza; all announcements will go there.

## Slide 18: Failure Detection in a Distributed System
That was for one process pj being detected and one process pi detecting failures
Let’s extend it to an entire distributed system
Difference from original failure detection is
  We want failure detection of not merely one process (pj), but all processes in system
Any idea?
  Why
  What
  How

## Slide 19: Efficiency of Failure Detector: Metrics
Bandwidth: the number of messages sent in the system during steady state (no failures)
  Small is good
Detection Time
  Time between a process crash and its detection
  Small is good
Scalability: Given the bandwidth and the detection properties, can you scale to a 1000 or million nodes?
  Large is good
Accuracy
  Large is good (lower inaccuracy is good)

## Slide 20: Accuracy Metrics
False Detection Rate: Average number of failures detected per second, when there are in fact no failures
Fraction of failure detections that are false
Tradeoffs: If you increase the T waiting period in ping-ack or 3*T waiting period in heartbeating what happens to:
  Detection Time?
  False positive rate?
  Where would you set these waiting periods?

## Slide 21: Centralized Heartbeat
…
pj, Heartbeat Seq. l++
pj
pi
Downside?

## Slide 22: Ring Heartbeat
pj, Heartbeat Seq. l++
pj
…
…
pi
Downside?

## Slide 23: All-to-All Heartbeat
pj, Heartbeat Seq. l++
…
pj
pi
Advantage: Everyone is able to keep track of everyone
Downside?

## Slide 24: Other Types of Failures
Let’s discuss the other types of failures
Failure detectors exist for them too (but we won’t discuss those)

## Slide 25: Processes and Channels
Outgoing message buffer
Incoming message buffer
Communication channel
Process p
Process q
receive
send m

## Slide 26: Other Failure Types
Communication omission failures
  Send-omission: loss of messages between the sending process and the outgoing message buffer (both inclusive)
    What might cause this?
  Channel omission: loss of message in the communication channel
    What might cause this?
  Receive-omission: loss of messages between the incoming message buffer and the receiving process (both inclusive)
    What might cause this?

## Slide 27: Other Failure Types
Arbitrary failures
  Arbitrary process failure: arbitrarily omits intended processing steps or takes unintended processing steps.
  Arbitrary channel failures: messages may be corrupted, duplicated, delivered out of order, incur extremely large delays; or non-existent messages may be delivered.
Above two are Byzantine failures, e.g., due to hackers, man-in-the-middle attacks, viruses, worms, etc.
A variety of Byzantine fault-tolerant protocols have been designed in literature!

## Slide 28: Omission and Arbitrary Failures
Class of failure
Affects
Description
Fail-stop
Process
Process halts and remains halted. Other processes may
detect this state.
Omission
Channel
A message inserted in an outgoing message buffer never
arrives at the other end’s incoming message buffer.
Send-omission
Process
A process completes a
send,
but the message is not put
in its outgoing message buffer.
Receive-omission
Process
A message is put in a process’s incoming message
buffer, but that process does not receive it.
Arbitrary
(Byzantine)
Process or
channel
Process/channel exhibits arbitrary behaviour: it may
send/transmit arbitrary messages at arbitrary times,
commit omissions; a process may stop or take an
incorrect step.

## Slide 29: Summary
Failure detectors are required in distributed systems to keep system running in spite of process crashes
Properties – completeness & accuracy, together unachievable in asynchronous systems but achievable in synchronous systems
  Most apps require 100% completeness, but can tolerate inaccuracy
2 failure detector algorithms - heartbeating and ping
Distributed FD through heartbeating: centralized, ring, all-to-all
Metrics: bandwidth, detection time, scale, accuracy
Other types of failures
Next: the notion of time in distributed systems

## Slide 30: Acknowledgements
These slides contain material developed and copyrighted by Indranil Gupta at UIUC.