## Slide 1: CSE 490/590 Computer Architecture Cache IV
Steve Ko
Computer Sciences and Engineering
University at Buffalo

## Slide 2: Last time…
Types of cache misses: 3 C’s
  Compulsory, Capacity, and Conflict
Write policies
  Write through vs. write back
  No write allocate vs. write allocate
Multi-level cache hierarchies reduce miss penalty
  Inclusive versus exclusive caching policy
  Can change design tradeoffs of L1 cache if known to have L2
Prefetching
  Speculate future I & D accesses and fetch them into caches
  Usefulness & timeliness

## Slide 3: Write-Back Cache Accesses
Write-back cache
  Writes only go to cache (make dirty lines)
  Upon evict, update memory
0 mem access
  Write hit
1 mem access
  Read miss on a clean line
2 mem accesses
  Read miss on a dirty line
Variable cycles per read/write, might complicate the pipeline control

## Slide 4: Hardware Instruction Prefetching
Instruction prefetch in Alpha AXP 21064
  Fetch two blocks on a miss; the requested block (i) and the next consecutive block (i+1)
  Requested block placed in cache, and next block in instruction stream buffer
  If miss in cache but hit in stream buffer, move stream buffer block into cache and prefetch next block (i+2)
L1 Instruction
Unified L2 Cache
RF
CPU
Stream
Buffer
Prefetched
instruction block
Req
block
Req
block
Notes: Need to check the stream buffer if the requested block is in there.
Never more than one 32-byte block in the stream buffer.

## Slide 5: Hardware Data Prefetching
Prefetch-on-miss:
  Prefetch b + 1 upon miss on b
One Block Lookahead (OBL) scheme
  Initiate prefetch for block b + 1 when block b is accessed
  Why is this different from doubling block size?
  Can extend to N-block lookahead
Strided prefetch
  If observe sequence of accesses to block b, b+N, b+2N, then prefetch b+3N etc.
Example: IBM Power 5 [2003] supports eight independent streams of strided prefetch per processor, prefetching 12 lines ahead of current access
Notes: HP PA 7200 uses OBL prefetching
Tag prefetching is twice as effective as prefetch-on-miss in
reducing miss rates.

## Slide 6: Software Prefetching
  for(i=0; i < N; i++) { prefetch( &a[i + 1] ); prefetch( &b[i + 1] ); SUM = SUM + a[i] * b[i]; }
What property do we require of the cache for prefetching to work ?
Notes: The processor should be able to proceed while the prefetched
Data is being fetched; and the caches continue to supply instructions
And data while waiting for the prefetched data to return.

## Slide 7: Software Prefetching Issues
Timing is the biggest issue, not predictability
  If you prefetch very close to when the data is required, you might be too late
  Prefetch too early, cause pollution
  Estimate how long it will take for the data to come into L1, so we can set P appropriately
  Why is this hard to do?
  for(i=0; i < N; i++) { prefetch( &a[i + P] ); prefetch( &b[i + P] ); SUM = SUM + a[i] * b[i]; }
Must consider cost of prefetch instructions

## Slide 8: Compiler Optimizations
Restructuring code affects the data block access sequence
  Group data accesses together to improve spatial locality
  Re-order data accesses to improve temporal locality
Prevent data from entering the cache
  Useful for variables that will only be accessed once before being replaced
  Needs mechanism for software to tell hardware not to cache data (“no-allocate” instruction hints or page table bits)
Kill data that will never be used again
  Streaming data exploits spatial locality but not temporal locality
  Replace into dead cache locations
Notes: Miss-rate reduction without any hardware changes.
Hardware designer’s favorite solution.

## Slide 9: Loop Interchange
  for(i=0; i < M; i++) { for(j=0; j < N; j++) { x[i][j] = 2 * x[i][j]; } }
What type of locality does this improve?
  for(j=0; j < N; j++) { for(i=0; i < M; i++) { x[i][j] = 2 * x[i][j]; } }

## Slide 10: Loop Fusion
  for(i=0; i < N; i++) a[i] = b[i] * c[i];
  for(i=0; i < N; i++)
  d[i] = a[i] * c[i];
  for(i=0; i < N; i++) { a[i] = b[i] * c[i]; d[i] = a[i] * c[i];
  }
What type of locality does this improve?

## Slide 11: Matrix Multiply, Naïve Code
  for(i=0; i < N; i++) for(j=0; j < N; j++) { r = 0; for(k=0; k < N; k++) r = r + y[i][k] * z[k][j]; x[i][j] = r; }
Not touched
Old access
New access
x
j
i
y
k
i
z
j
k

## Slide 12: Matrix Multiply with Cache Tiling
  for(jj=0; jj < N; jj=jj+B) for(kk=0; kk < N; kk=kk+B) for(i=0; i < N; i++) for(j=jj; j < min(jj+B,N); j++) { r = 0; for(k=kk; k < min(kk+B,N); k++) r = r + y[i][k] * z[k][j]; x[i][j] = x[i][j] + r; }
What type of locality does this improve?
y
k
i
z
j
k
x
j
i
Notes: Y benefits from spatial locality
z benefits from temporal locality

## Slide 13: CSE 490/590 Administrivia
Midterm on Friday, 3/4
Project 1 deadline: Friday, 3/11
Guest lectures possibly this month
Course early-evaluation today

## Slide 14: Acknowledgements
These slides heavily contain material developed and copyright by
  Krste Asanovic (MIT/UCB)
  David Patterson (UCB)
And also by:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252