## Slide 1: CSE 490/590 Computer Architecture Synchronization and Consistency II
Steve Ko
Computer Sciences and Engineering
University at Buffalo

## Slide 2: Last time…
Consistency problem
  Producer-consumer
Sequential consistency
Semaphores
Instructions that can implement semaphores
  Test&set
  Fetch&add
  Swap

## Slide 3: Locks or Semaphores E. W. Dijkstra, 1965
A semaphore is a non-negative integer, with the
following operations:
  P(s): if s>0, decrement s by 1, otherwise wait
  V(s): increment s by 1 and wake up one of
  the waiting processes
P’s and V’s must be executed atomically, i.e., without
  interruptions or
  interleaved accesses to s by other processors
initial value of s determines
the maximum no. of processes
in the critical section
Process i
  P(s)
  <critical section>
  V(s)

## Slide 4: Implementation of Semaphores
Semaphores (mutual exclusion) can be implemented
using ordinary Load and Store instructions in the
Sequential Consistency memory model. However,
protocols for mutual exclusion are difficult to design...
Simpler solution:
atomic read-modify-write instructions
Test&Set (m), R:
  R  M[m];
  if R==0 then
M[m] 1;
Swap (m), R:
  Rt  M[m];
  M[m] R;
  R  Rt;
Fetch&Add (m), RV, R:
  R  M[m];
  M[m] R + RV;
Examples: m is a memory location, R is a register

## Slide 5: Multiple Consumers Example using the Test&Set Instruction
Critical
Section
P: Test&Set (mutex),Rtemp
if (Rtemp!=0) goto P
Load Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead=Rhead+1
Store (head), Rhead
V: Store (mutex),0
process(R)
Other atomic read-modify-write instructions (Swap,
Fetch&Add, etc.) can also implement P’s and V’s
What if the process stops or is swapped out while in the critical section?

## Slide 6: Nonblocking Synchronization
Compare&Swap(m), Rt, Rs:
if (Rt==M[m])
then M[m]=Rs;
Rs=Rt ;
status success;
else status fail;
try: Load Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rnewhead = Rhead+1
Compare&Swap(head), Rhead, Rnewhead
if (status==fail) goto try
process(R)
status is an implicit argument

## Slide 7: Load-reserve & Store-conditional
Special register(s) to hold reservation flag and address,
and the outcome of store-conditional
try: Load-reserve Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead = Rhead + 1
Store-conditional (head), Rhead
if (status==fail) goto try
process(R)
Load-reserve R, (m):
  <flag, adr>  <1, m>;
  R  M[m];
Store-conditional (m), R:
  if <flag, adr> == <1, m>
  then cancel other procs’
  reservation on m;
    M[m] R;
    status succeed;
  else status fail;

## Slide 8: Performance of Locks
Blocking atomic read-modify-write instructions
e.g., Test&Set, Fetch&Add, Swap
vs
Non-blocking atomic read-modify-write instructions
e.g., Compare&Swap,
Load-reserve/Store-conditional
vs
Protocols based on ordinary Loads and Stores
Performance depends on several interacting factors:
degree of contention,
caches,
out-of-order execution of Loads and Stores
later ...

## Slide 9: Issues in Implementing Sequential Consistency
Implementation of SC is complicated by two issues
  Out-of-order execution capability
      Load(a); Load(b) yes
      Load(a); Store(b) yes if a  b
      Store(a); Load(b) yes if a  b
      Store(a); Store(b) yes if a  b
  Caches
    Caches can prevent the effect of a store from
    being seen by other processors
M
P
P
P
P
P
P

## Slide 10: CSE 490/590 Administrivia
No class on Friday, 4/15
Keyboards available for pickup at my office
  Today after 2pm

## Slide 11: Memory Fences Instructions to sequentialize memory accesses
Processors with relaxed or weak memory models (i.e.,
permit Loads and Stores to different addresses to be
reordered) need to provide memory fence instructions
to force the serialization of memory accesses
Examples of processors with relaxed memory models:
  Sparc V8 (TSO,PSO): Membar
  Sparc V9 (RMO):
  Membar #LoadLoad, Membar #LoadStore
Membar #StoreLoad, Membar #StoreStore
  PowerPC (WO): Sync, EIEIO
Memory fences are expensive operations, however, one
pays the cost of serialization only when it is required

## Slide 12: Using Memory Fences
Producer posting Item x:
Load Rtail, (tail)
Store (Rtail), x
MembarSS
Rtail=Rtail+1
Store (tail), Rtail
Consumer:
Load Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
MembarLL
Load R, (Rhead)
Rhead=Rhead+1
Store (head), Rhead
process(R)
Producer
Consumer
tail
head
Rtail
Rtail
Rhead
R
ensures that tail ptr
is not updated before
x has been stored
ensures that R is
not loaded before
x has been stored

## Slide 13: Mutual Exclusion Using Load/Store
A protocol based on two shared variables c1 and c2.
Initially, both c1 and c2 are 0 (not busy)
What is wrong?
Process 1
  ...
  c1=1;
L: if c2=1 then go to L
  < critical section>
  c1=0;
Process 2
  ...
  c2=1;
L: if c1=1 then go to L
  < critical section>
  c2=0;

## Slide 14: Mutual Exclusion: second attempt
To avoid deadlock, let a process give up the reservation
(i.e. Process 1 sets c1 to 0) while waiting.
Deadlock is not possible but with a low probability
a livelock may occur.
An unlucky process may never get to enter the
critical section  starvation
Process 1
  ...
L: c1=1;
  if c2=1 then
{ c1=0; go to L}
  < critical section>
  c1=0
Process 2
  ...
L: c2=1;
  if c1=1 then
{ c2=0; go to L}
  < critical section>
  c2=0

## Slide 15: Acknowledgements
These slides heavily contain material developed and copyright by
  Krste Asanovic (MIT/UCB)
  David Patterson (UCB)
And also by:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252