NEXOS LAB GUIDELINE

- Log in on any computer in the lab

- Start Putty

- Type the host-name as nexos-dlink.cse.buffalo.edu

  - When you are off-campus, connect nickelback or hadar first and then use command ssh nexos-dlink.cse.buffalo.edu

- Enter your ubit-name and password (your password is your person #)

  - Change your password using command passwd

- Go to the folder where you have the .boot file

  - We strongly recommend you to use and keep the directory structure initially created.

  - Compile directory has all things needed for the compilation and compiled xinu.boot file.

  - Use make command to compile the source files.

- Check out available routers before you use one. The command is xinu-status.

  - Router names are listed above. If there’s a name in the user field, the user is using the router. Select another available one.

  - Router names followed by 1 are the second serial port of the router named without 1.

- To boot the router with xinu boot image, use mips-console router-name command (see the example below). The boot image should be named xinu.boot (default name). You will see booting procedure similar one shown below.

- To exit or terminate xinu, press ctrl+spacebar and then press q. You can see available commands by press ?.

- YOU MUST EXIT AND RELEASE THE ROUTER YOU USED FOR OTHER STUDENTS.