## Slide 1: More on Cyclic Executives
Simple loop cyclic executive
Frame/slots
Table-based predetermined schedule cyclic executive
Periodic, aperiodic and interrupt-based task
Lets design a cyclic-executive with multiple periodic tasks.
1

## Slide 2: The basic systems
Several functions are called in a prearranged sequence
Some kind of cooperative scheduling
You a have a set of tasks and a scheduler that schedules these tasks
Types of tasks: base tasks (background), interrupt tasks, clock tasks
Frame of slots, slots of cycles, each task taking a cycle, burn tasks to fill up the left over cycles in a frame.
2

## Slide 3: Cyclic Executive Design 1 (pages 81-87)
Base tasks, clock tasks, interrupt tasks
  Base: no strict requirements, background activity
  Clock: periodic with fixed runtime
  Interrupt: event-driven preemption, rapid response but little processing
Design the slots
Table-driven cyclic executive

## Slide 4: Cyclic executive
Each task implemented as a function
All tasks see global data and share them
Cyclic executive for three priority level
The execution sequence of tasks within a cyclic executive will NOT vary in any unpredictable manner (such as in a regular fully featured Operating Systems)
Clock tasks, clock sched, base tasks, base sched, interrupt tasks
Each clock slot executes, clock tasks, at the end a burn task that is usually the base task
Study the figures in pages 83-86 of your text

## Slide 5: RT Cyclic Executive Program
Lets examine the code:
Identify the tasks
Identify the cyclic schedule specified in the form of a table
Observe how the functions are specified as table entry
Understand the scheduler is built-in
Learn how the function in the table are dispatched

## Slide 6: Implementation of a cyclic executive
#include <stdio.h>
#include <ctype.h>
#include <unistd.h>
#include <sys/times.h>
#define SLOTX 4
#define CYCLEX 5
#define SLOT_T 5000
int tps,cycle=0,slot=0;
clock_t now, then;
struct tms n;
void one() {
printf("Task 1 running\n");
sleep(1);
}
void two() {
printf("Task 2 running\n");
sleep(1); }

## Slide 7: Implementation (contd.)
void three() {
printf("Task 3 running\n");
sleep(1);
}
void four() {
printf("Task 4 running\n");
sleep(1);
}
void five() {
printf("Task 5 running\n");
sleep(1);
}

## Slide 8: Implementation (contd.)
void burn() {
clock_t bstart = times(&n);
while ((( now = times(&n)) - then) < SLOT_T * tps / 1000) { }
printf (" brn time = %2.2dms\n\n", (times(&n)-bstart)*1000/tps);
then = now;
cycle = CYCLEX;
}

## Slide 9: Implementation (contd.)
void (*ttable[SLOTX][CYCLEX])() = {
{one, two, burn, burn, burn},
{one, three, four, burn, burn},
{one, two, burn, burn, burn},
{one, five, four, burn, burn}};
main() {
tps = sysconf(_SC_CLK_TCK);
printf("clock ticks/sec = %d\n\n", tps);
then = times(&n);
while (1) {
for (slot=0; slot <SLOTX; slot++)
for (cycle=0; cycle<CYCLEX; cycle++)
(*ttable[slot][cycle])();
}}

## Slide 10: Summary
The cyclic executive discussed the scheduler is built-in. You can also use clock ticks RTC etc to schedule the tasks
In order use the cyclic executive discussed here in other applications simply change table configuration, and rewrite the dummy functions we used.