## Slide 1: CSE 490/590 Computer Architecture Snoopy Caches II
Steve Ko
Computer Sciences and Engineering
University at Buffalo

## Slide 2: Last time…
Cache coherence protocol
  How to propagate writes by one processor to others
Cache coherence protocol vs. memory consistency
  Cache coherence protocol makes sure that writes are eventually propagated.
  Memory consistency protocol guarantees when writes become visible.

## Slide 3: More on Coherence
A memory system is coherent if:
A read by a processor P to a location X that follows a write by P to X, with no writes of X by another processor occurring between the write and the read by P, always returns the value written by P.
A read by a processor to location X that follows a write by another processor to X returns the written value if the read and write are sufficiently separated in time and no other writes to X occur between the two accesses.
Writes to the same location are serialized; that is, two writes to the same location by any two processors are seen in the same order by all processors.

## Slide 4: Memory Coherence in SMPs
Suppose CPU-1 updates A to 200.
write-back: memory and cache-2 have stale values
write-through: cache-2 has a stale value
Do these stale values matter?
What is the view of shared memory for programming?
cache-1
A 100
CPU-Memory bus
CPU-1
CPU-2
cache-2
A 100
memory
A 100

## Slide 5: Problems with Parallel I/O
Memory Disk: Physical memory may be
stale if cache copy is dirty
Disk Memory: Cache may hold stale data and not see memory writes
DISK
DMA
Physical
Memory
Proc.
Cache
Memory
Bus
Cached portions
of page
DMA transfers

## Slide 6: Snoopy Cache Goodman 1983
Idea: Have cache watch (or snoop upon) DMA transfers, and then “do the right thing”
Snoopy cache tags are dual-ported
Proc.
Cache
Snoopy read port
attached to Memory
Bus
Data
(lines)
Tags and
State
A
D
R/W
Used to drive Memory Bus
when Cache is Bus Master
A
R/W

## Slide 7: Snoopy Cache Actions for DMA
Observed Bus Cycle Cache State Cache Action
Address not cached
DMA Read Cached, unmodified
Memory Disk Cached, modified
Address not cached
DMA Write Cached, unmodified
Disk Memory Cached, modified
No action
No action
No action
Cache intervenes
Cache purges its copy
???

## Slide 8: Shared Memory Multiprocessor
Use snoopy mechanism to keep all processors’ view of memory coherent
M1
M2
M3
Snoopy
Cache
DMA
Physical
Memory
Memory
Bus
Snoopy
Cache
Snoopy
Cache
DISKS

## Slide 9: Snoopy Cache Coherence Protocols
write miss:
  the address is invalidated in all other
  caches before the write is performed
read miss:
  if a dirty copy is found in some cache, a write-back is performed before the memory is read
Notes: Update protocols, or write broadcast. Latency between writing a word in one processor
and reading it in another is usually smaller in a write update scheme.
But since bandwidth is more precious, most multiprocessors use a write invalidate scheme.

## Slide 10: Cache State Transition Diagram The MSI protocol
M
S
I
M: Modified
S: Shared
I: Invalid
Each cache line has state bits
Address tag
state
bits
Write miss
(P1 gets line from memory)
Other processor
intent to write (P1 writes back)
Read miss
(P1 gets line from memory)
P1 intent to write
Other processor
intent to write
Read by any
processor
P1 reads
or writes
Cache state in processor P1
Other processor reads
(P1 writes back)

## Slide 11: Two Processor Example (Reading and writing the same cache line)
M
S
I
Write miss
Read
miss
P1 intent to write
P2 intent to write
P2 reads,
P1 writes back
P1 reads
or writes
P2 intent to write
P1
M
S
I
Write miss
Read
miss
P2 intent to write
P1 intent to write
P1 reads,
P2 writes back
P2 reads
or writes
P1 intent to write
P2
P1 reads
P1 writes
P2 reads
P2 writes
P1 writes
P2 writes
P1 reads
P1 writes

## Slide 12: Observation
If a line is in the M state then no other cache can have a copy of the line!
  Memory stays coherent, multiple differing copies cannot exist
M
S
I
Write miss
Other processor
intent to write
Read
miss
P1 intent to write
Other processor
intent to write
Read by any
processor
P1 reads
or writes
Other processor reads
P1 writes back

## Slide 13: MESI: An Enhanced MSI protocol increased performance for private data
M
E
S
I
M: Modified Exclusive
E: Exclusive but unmodified
S: Shared
I: Invalid
Each cache line has a tag
Address tag
state
bits
Write miss
Other processor
intent to write
Read miss,
shared
Other processor
intent to write
P1 write
Read by any
processor
Other processor reads
P1 writes back
P1 read
P1 write
or read
Cache state in processor P1
P1 intent to write
Read miss, not shared
Other processor
reads
Other processor intent to write, P1 writes back

## Slide 14: CSE 490/590 Administrivia
Keyboards available for pickup at my office
Project 2: 2 weeks left (Deadline 5/2)
  Will have demo sessions
  Keyboard helper code will be available
Final exam: Thursday 5/5, 11:45pm – 2:45pm

## Slide 15: Acknowledgements
These slides heavily contain material developed and copyright by
  Krste Asanovic (MIT/UCB)
  David Patterson (UCB)
And also by:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252